Wireless Termination Points Configuration.

The daemon is located in /etc/init.d/empower
enable	the daemon is enabled at every boot
start	the daemon is started
reload	reloads the configuration

The daemon reads the configurations files and adds a ovs bridge named br-ovs after is adds the ports eth0.1 and empower0 to the bridge. The openvswitch controller is also set with the same ip address of empower server.

The configuration files.

/etc/config/network

#default for nanostation
config switch
  option name 'switch0'
  option reset '1'
  option enable_vlan '1'

config switch_vlan
  option device 'switch0'
  option vlan '1'
  option ports '0t 5'

config switch_vlan
  option device 'switch0'
  option vlan '2'
  option ports '0t 1'

config interface 'loopback'
  option ifname 'lo'
  option proto 'static'
  option ipaddr '127.0.0.1'
  option netmask '255.0.0.0'

config globals 'globals'
  option ula_prefix 'fd37:b8cb:1142::/48'

#actual configuration
config device
  option name 'br-ovs'	#bridge name
  option type 'ovs'
    list ifname 'eth0.1'	#bridge ports

    config interface 'lan'	#must be the same with empower configuration
        option 'ifname' 'br-ovs'
        option 'proto' 'static'
        option ipaddr '10.123.0.15'
        option netmask '255.255.255.0'
        option gateway '10.123.0.254'	#if we need the WTPs to connect to internet
        option dns '8.8.8.8'

/etc/config/empower

 config empower general
    option "master_ip" "10.123.0.254"	#ip of the controller
    option "master_port" "4433"
    option "network" "lan"	#network name
    option "interface" "empower0"
    option "static_rate" "false"
    option "no_rx_stats" "false"
    option "no_stats" "false"
    option "no_signalling_stats" "false"
    list "ifname" "empower0"

    list "debugfs" "/sys/kernel/debug/ieee80211/phy0/ath9k/bssid_extra"

/etc/config/wireless
config wifi-device radio0
        option type mac80211
        option channel 36
        option hwmode 11a
        option path 'platform/ar934x_wmac'

       config wifi-iface empower0
        option device radio0
        option mode monitor
        option ifname moni0

On the controller

/etc/network/interfaces

#The OVS bridge interface
auto br0
iface br0 inet static
address 10.123.0.254
netmask 255.255.255.0
bridge_ports eth1
bridge_fd 9
bridge_hello 2
bridge_maxage 12
bridge_stp off